Clock thermostat with segments, daily program, operating mode switch (RAM 722 s)

Electronic thermostat with automatic temperature reduction at night; 24 hour segment program disc; programmable every 15 minutes; shortest switching time; day and night temperature settings from +10°C ... 30°C; operating mode switch; frost protection 6°C; party switch; indicator display; thermal circulation and operating point settings; housing colour: white; 1 two way switch 6A/250V~.

Deliver, assemble, connect up and set up

...

Make: Theben

Type: RAM 722 s

Order No.: 7220801

Unit: ST