Rail mounted digital timer 1 channel, DCF, 7 days, control input, pulse, cycle, plug clamp 2 TLE (TR 611 top2 DCF ( or antenna with power unit))

Rail mounted digital timer with DCF77 controlled time; text-oriented user guidance and backlit display; interface incl. OBELISK top2 memory card; width 35 mm; spring screwless terminals; 10 year power reserve and programmed summer/winter changeover. Daily and weekly program; shortest switching time 1 minute; holiday, pulse and cycle program; 2 random programs; delay timer; external control input; permanent ON/OFF/AUTO switching; switching pre-selection; 84 memory locations; PIN code; 1 channel; 1 two way switch 16A/250 V~

Deliver, assemble, connect up and set up

...

Make: Theben

Type: TR 611 top2 DCF (or antenna with power unit)

Order no.: 6110300

# Unit: ST

Accessories:

Antenna top2 RC-DCF max. 10 TERMINA top2, LUNA top2 or SELEKTA top2 devices can be connected

Order no.: 9070410